## Slide 1: ELEVATING TRAFFIC BARRICADES

## Slide 2: PRESENTED BY
BATCH NO. A8
1.D.Varsha (19R01A0417)
2. G.Mahesh (19R01A0425)
3.M.kavya sree (19R01A0435)
4. M.Vishnu (19R01A0436)
5.MV.Pavan Rahul (19R01A0437)
6. V.Uday kiran (19R01A0455)

## Slide 3: CONTENTS
PROBLEM DEFINATION
LITERATURE SURVEY
PROPOSED IDEA
METHODOLOGY
WORKING PRINCIPLE
ADVANTAGES
APPLICATIONS
CONCLUSION
REFERENCE

## Slide 4: PROBLEM DEFINITION
With the growth of the urbanization, industrialization and population, there has been a tremendous growth in the traffic. There is occurrence of bundle of problems too, these problems include signal jump, traffic jams, accidents and traffic rule violation. In 1868, the traffic lights only installed in London and today these have installed in every cities around the world. Today red light violation is one of the most common and serious problem which results in the collision of millions of vehicles at the traffic light signals every year. A red light violation occurs when a vehicle try to cross the intersection at the red traffic light.

## Slide 5: LITERATURE SURVEY
Survey Report:
Goal name: Traffic barricades
Team name: Sadak suraksha
Survey place: Lingampally 4 road junction
Date of the survey: 1st December 2019
Members who attended the survey:
Pavan Rahul
Uday kiran
Varsha
Summary:We spoke to the traffic police Mr Rajesh kumar . We asked different problems on jumping the traffic signals . He said jumping the signals causes serious impact on person who drives . He even said he will be facing the consequences.
Events which can be conducted:
We spoke to him about our project (traffic barricades) he was very interested on hearing about our project he expressed
Success of the survey: 10/10
Scope of success of the event: 10/10

## Slide 6: PROPOSED IDEA
After considering the problem we have discussed with our team and came out with an innovative idea The elevating traffic barricades . Even after imposing heavy fines for jumping the signal many of them violate,Therefore if we install elevating traffic barricades near traffic signals when the signals turns red the barricades start to elevate from the ground surface which blocks the vehicles from jumping the signal.

## Slide 7: WORKING PRINCIPLE
Retractable bollards can be lowered entirely below the road surface to allow traffic to pass, or raised to block traffic or to enforce traffic rules that are time related.
Automatic Rising Bollards are equipped with compact hydraulic unit built with pump piston drive mechanism that makes it more suitable for smooth operations .
Performance: Automatic Rising Barricades characterized by high efficiency and complete performance. They are impeccable in their movement .
Intelligent Control Unit with versatile configuration makes it more flexible for different applications and integration. Intelligent unit provides unique feature and master slave kit allow smooth operation for entire set of barricades.
Safe: In-built hydraulic accumulator that allows, in case of emergency and with a specific command, to lift the bollard immediately and in-built pressure switch provide more safety by lowering down the bollard detection of any object during movement.

## Slide 8: ADVANTAGES
Blocks vehicles from jumping signal
They Restrict Access
These bollards quickly separate traffic from pedestrians

## Slide 9: APPLICATIONS
• It protects loading bays or roller shutters from ram-aid attack
• It allows only authorized types of vehicles onto the premises
• It ensures that drivers pay the parking fees at private parking sector
• It also prevents the general public from entering restricted zones
• Even it also prevent vehicles from encroaching into pedestrian zones Uses of automatic bollards

## Slide 10: MEDHODOLOGY
Manufacturing of bollard system is done by using different performance categories, testing
methods, design calculations and guidelines .
Design Calculation:
Electro-Hydraulic Bollard consists of 3 cylinders of same sizes viz. Bore Diameter (D): 32mm, Piston Rod diameter (d): 25 mm, Stroke Lengthfrom BDC to TDC (S): 760 mm. Stroke Timing (ST)from BDC to TDC & vice-versa: 5 seconds. TotalForce/Weight on 3 cylinders (F): 2.5 tons.
Cylinder calculations are as follows:
Area of Bore Side of each Cylinder:?? = ????
2
/4.
AB =
0.785*3.2*3.2 cm2
AB = 8.04
cm2
? ABT = 3* AB
? ABT = 3*8.04 cm2
? ABT = 24.12 cm2
Area of Annulus Side of each Cylinder: ?? =
??(??
2 - ??
2
)/4.
AA =
0.785*(3.2*3.2-2.5*2.5) cm2
AA= 3.13 cm2
? AAT = 3* AA
? AAT = 3*3.13 cm2
? AAT = 9.39 cm2

## Slide 11
Volume required for each Cylinder: V =Area * Stroke Length.
Volume required on Bore Side of each cylinder:
VB=AB *S.
? 8.04 * 76 cm3
? 611.04 cm3 (Now 1 cm3 = .001 ltrs)
? 0.61 ltrs
For 3 nos. of Cylinders: VBT : VB *3 liters
VBT : 0.61*3 liters
VBT : 1.83 liters
Volume required on Bore Side of each cylinder:
AA*S.
? 3.13 * 76 cm3
? 237.88 cm3 (Now 1 cm3 = .001 liters)
? 0.238 liters
For 3 nos. of Cylinders: VAT : VA*3 liters
VAT : 0.238*3 liters
VAT : 0.71 liters
The three Cylinders have to operate within 5 seconds to lift the Bollard & to perform required safety operations. For this we need to provide the fluid to the Bore side of the Cylinder at a particular flow rate that could meet the function.
Similarly fluid needs to be admitted to Annulus side of the cylinder to retract the cylinder down. For this we will be requiring a Hydraulic oil Pump with a specific flow rate that could lift the cylinder up-to its full stroke length within the specified timing. Flow rate required to Lift/Retract the cylinders to full stroke length: (Volume/Stroke timing) liters per minute.
Flow Rate required to Lift the cylinders: QBT : VBT /T
(1.83 *60) /5 liters per minute
22 liters per minute.
? Flow Rate required to retract the cylinders:
QAT: VAT / ST
? (0.71 *60) /5 liters per minute 9 liters per
minute
Since the maximum Flow rate required is during Lifting hence the pump flow is selected according to the Lifting operation requirements. Also since it is a mechanical system there will be losses like slippage, leakages etc. which needed to be compensated & therefore a margin over the required flow rate is required.

## Slide 12
We have considered 20% margin over the required
flow rate i.e.: Required flow rate * 1.20
? 22*1.20 liters per minute
? 26.4 liters per minute
? Approx. 27 liters per minute.
The Pressure required to Lift the cylinders against the load is calculated using Pascal’s Law which states that:
Pressure = (Force or Weight/Area) Kg/cm2 or bar
Hence, Pressure Require for Lifting the Cylinders:
PBT = Force/ ABT
? PBT = 2500/24.12 Kg/Cm2
PBT = 103.6 Kg/Cm2
Due to mechanical System there will be some losses such as heat, pressure drop across valves & in Pipes/Tubes; we have taken 10% margin over the
required pressure for lifting.
Therefore the Design pressure is taken as: PD - PBT *
1.1
? PD = 103.6*1.1 Kg/Cm2
? PD = 115 Kg/Cm2
The Hydraulic Oil Pump can be of different types such as External Gear Pump, Vane Pump, variable displacement axial piston Pump, and Internal gear Pump etc. Any of these pumps can be used depending on the application of the system. Now for driving the Hydraulic oil pump we need an AC Electric Motor of a particular rating. The Motor rating depends upon three factors viz. Pressure, Flow & efficiency of the Pump.
Motor kW can be calculated by below given formula:
1. Motor Rating (kW):- (Pressure X Flow
rate)/(600 X Overall efficiency of Oil Pump)
Efficiency of Oil Pump varies from type to type:
1. Variable Displacement Axial piston pump
: 90%
2. External Gear Pump : 65%
3. Internal Gear Pump : 75%

## Slide 13: CONCLUSION
Traffic Barricades Are Designed To Offer An Impactresistant Barrier To Vehicle Access Near Traffic Signals , Whilst Allowing Access To Pedestrians ,At Preasent Due To The Poor Management Of Traffic Management Number Of People Are Voilating The Traffic Rules Jumping The Signals Even After Imposing Heafty Fines They Tend To Do This .Therby We Want To Conclude Implementing The Traffic Barricdes Will Stop Everyone Jumping The Signas Saving Numbre Of Lives.